## Slide 1: POSIX Pipelines
Rick Troth
2023 June 14

## Slide 3: Hartmann History Here
Pursuing a Pipeline that works like Hartmann Pipes, but for POSIX
Invokation syntax to follow the syntax of CMS/TSO Pipelines
Stages run as independent processes (not just as threads)
Impose minimal required infrastructure (e.g., no JVM needed)

## Slide 4: Plumbing for POSIX with pipe() pair
POSIX pipe() system call returns a pair of file descriptors at the ends of a “leaky garden hose”
write() does not block at record boundaries, but read() blocks until something is available
Use a pair of POSIX pipes to simulate a Hartmann connector
Producer does a read() on a reverse pipe until consumer says “go” then sends the record down the forward pipe and waits for “done” from consumer

## Slide 5: Plumbing for POSIX with pipe() pair
POSIX plumbing is slow.
Start with that because it is known to work.
Switch to using shared memory when/where that is available.

## Slide 6: POSIX Plumbing Program
‘pipe’ command from any shell
Follows CMS/TSO Pipelines syntax but also does Unix style
Parser splits the (quoted*) pipeline into stages *so that the shell doesn’t get involved
Dispatcher arranges file descriptors for individual stages then spawns them
Stages inherit open file descriptors and env vars describing them
Stages are programs but not found via PATH variable
The whole thing waits until done like a shell

## Slide 7: Passing Connectors
Connector Descriptor passed from dispatcher to stages
*. [input|output] . [name|number] : fdfwd , fdrev
Asterisk, dot, “INPUT” or “OUTPUT”
Dot, stream name or stream number
Colon, forward file descriptor, comma, reverse file descriptor

## Slide 8: Passing Connectors
Connector Descriptors are passed in the POSIX “environment”.
The dispatcher sets the environment variable PIPECONNS uniquely for each stage as it spawns that stage. The variable contains a string of multiple connector specifications following the syntax shown:
*. [input|output] . [name|number] : fdfwd , fdrev
File descriptors opened by the dispatcher and inherited by the stages

## Slide 9: Flow Protocol – sending a record
Producer has 1234 bytes to send, calls an ‘OUTPUT’, passes metadata and blocks
After consumer returns “NEXT”, producer sends “OKAY” and unblocks
Consumer issues a ‘READTO’ and drives the transaction. It confirms that its buffer can hold the record coming, returns “PEEK” and reads, returns “NEXT”, then unblocks
fdforward fdreverse
← “STAT”
“DATA 1234” →
← “PEEK 1234”
1234 bytes of data →
← “NEXT”
“OKAY” →

## Slide 10: Flow Protocol – previewing a record
Producer has 1234 bytes to send, calls an ‘OUTPUT’, passes metadata and blocks
When consumer returns “PEEK”, producer restarts
Consumer issues a ‘PEEKTO’ and drives the transaction. It confirms that its buffer can hold the record coming, returns “PEEK” and reads, then unblocks
fdforward fdreverse
← “STAT”
“DATA 1234” →
← “PEEK 1234”
1234 bytes of data →
This does not unblock the producer